# Booting Process of Raspberry Pi 4
### 1. Power On & Boot ROM
- When you power up, the Boot ROM (hardcoded inside the Broadcom SoC) is the very first code to run.
- It runs on the GPU (VideoCore VI), not the ARM CPU (the CPU is still in reset).
- The Boot ROM:
  - Reads the SPI EEPROM to find the 2nd-stage bootloader.
  - If EEPROM is missing or corrupted → it enters recovery mode (USB mass storage device or flashes screen with diagnostics).

### 2. EEPROM Bootloader
- The Pi 4 has a small SPI EEPROM that contains the 2nd-stage bootloader.
- This EEPROM bootloader is upgradable (rpi-eeprom-update).
- Tasks:
  - Initializes LPDDR4 RAM.
  - Reads the boot configuration (boot order, retry attempts, etc.) from the EEPROM.
  - Tries boot devices in order:
    - SD card (default)
    - USB mass storage (SSD/HDD/flash drive)
    - Network boot (PXE)
    - (Pi 5 only adds NVMe boot)
  - Once a boot device is found, it loads start.elf (GPU firmware).

### 3. GPU Firmware (start.elf)
- Runs entirely on the GPU, not CPU.
- This is the main firmware blob provided by the Raspberry Pi Foundation.
- Responsibilities:
  - Initialize clocks, power, HDMI, USB, and other peripherals.
  - Read config.txt (user boot configuration file in FAT32 boot partition).
  - Read cmdline.txt (kernel command line arguments).
  - Load the Device Tree Blob (.dtb) (describes hardware to Linux).
  - Load the Linux kernel image (kernel8.img for 64-bit, kernel7l.img for 32-bit).
👉 At this point, everything the kernel needs is ready in memory.

### 4. ARM CPU Release
- Until now, the ARM Cortex-A72 CPU cores were held in reset.
- Now the GPU firmware releases the ARM CPU, handing control to the Linux kernel.
- The CPU starts executing kernel instructions.

### 5. Linux Kernel Initialization
- The Linux kernel initializes:
  - Virtual memory & MMU
  - Device drivers (USB, Ethernet, GPIO, I2C, SPI, etc.)
  - Mounts the root filesystem (ext4, NFS, USB, etc.)
- Loads init (PID 1) or systemd as the first user-space process.

### 6. Userland
- Userland services (login manager, desktop environment, daemons) are started.
- Raspberry Pi is now fully booted and ready for user interaction.

# 🔹 Summary of Raspberry Pi 4 Boot Stages
1. Boot ROM (SoC) → looks in EEPROM.
2. EEPROM Bootloader → initializes RAM, checks boot order, loads GPU firmware.
3. GPU Firmware (start.elf) → reads config.txt, loads kernel + device tree, releases CPU.
4. ARM CPU (Kernel) → initializes hardware, mounts rootfs, starts init.
5. Userland → services, desktop, or shell.
## Raspberry Pi 4 Boot Process
### 1. Power-On and Reset
- When you apply power (5V via USB-C or GPIO), the SoC (Broadcom BCM2711) comes out of reset.
- Unlike older Pis (which used the GPU to boot), the Pi 4 has a small on-chip ROM bootloader (called BootROM).
- This BootROM is hardcoded into the SoC and cannot be changed. Its job is to locate the next stage of booting.

### 2. BootROM Execution
- The BootROM is the first code executed.
- It looks for bootable media in a fixed order (configurable via bootloader EEPROM):
  - SPI EEPROM (onboard flash containing the next-stage bootloader).
  - If SPI EEPROM is valid → Boot from there.
  - If not, fallback options: SD card, USB, network boot (if enabled).
✅ On Pi 4, the primary bootloader is stored in EEPROM, not on the SD card like Pi 3.

### 3. EEPROM Bootloader
- The SPI EEPROM contains a small but updatable bootloader.
- It decides where to boot from (SD card, USB, network).
- You can update this EEPROM using Raspberry Pi tools if needed.
- If EEPROM is corrupted → Green LED blinks a specific error code.

### 4. Loading bootcode (from SD/USB)
- Once the EEPROM bootloader picks a device (say SD card), it looks for the boot partition.
- On the SD card, the first partition is FAT32 and contains boot files.
- The EEPROM bootloader loads start4.elf (the GPU firmware) and fixup4.dat.

### 5. GPU Firmware Execution
- On Raspberry Pi, the GPU starts first, not the ARM CPU.
- start4.elf is a closed-source firmware blob that initializes the GPU, memory, and hardware.
- It also reads config.txt from the SD card → applies user settings (CPU/GPU split, HDMI options, overlays, etc.).

### 6. Loading U-Boot / Kernel
- Depending on the setup:
  - By default, the firmware loads the Linux kernel (kernel8.img) directly.
  - If you installed U-Boot, the firmware loads U-Boot first, then U-Boot loads the kernel.
- cmdline.txt contains kernel boot parameters (like root filesystem location).

### 7. ARM CPU Start
- The GPU firmware releases control of the ARM CPU cores.
- The ARM CPU executes the Linux kernel (or other OS kernel).
- The kernel mounts the root filesystem (from SD, USB, or network).

### 8. Init Process (Linux userspace)
- The kernel starts /sbin/init (or systemd).
- From here, your normal Linux OS starts:
  - Drivers load
  - Services start
  - Login prompt or GUI appears

## Summary of Raspberry Pi 4 Boot Flow
1. Power On → SoC resets.
2. BootROM → Runs from chip, checks SPI EEPROM.
3. EEPROM Bootloader → Decides boot device (SD, USB, network).
4. SD/USB Boot Partition → Loads start4.elf + fixup4.dat.
5. GPU Firmware → Initializes system, reads config.txt.
6. Kernel/U-Boot → Loaded from SD/USB.
7. ARM CPU Runs Kernel → Linux starts.
8. Init Process → Services → User login.