PCI stands for Peripheral Component Interconnect. It’s a standard bus architecture used in computers to connect peripheral devices (like network cards, sound cards, graphics cards, storage controllers, etc.) to the motherboard.
What PCI Does:

Provides a way for the CPU to communicate with external devices.

Allows multiple devices to share the same bus.

Supports plug-and-play — devices can be added or removed without configuring jumpers manually.

Supports 32-bit or 64-bit data paths and operates at various clock speeds depending on the PCI version.

Key Points:

Developed by Intel in the early 1990s.

Standard PCI slots are commonly found on desktop motherboards.

PCI Express (PCIe) is the modern replacement, offering faster data transfer rates using serial communication.

Devices on PCI have unique addresses and can issue interrupts to the CPU.

Summary:

PCI is a hardware interface standard that enables expansion cards and devices to communicate efficiently with the computer’s CPU and memory over a common bus.

If you want, I can also explain PCI Express or how PCI works internally!
You said:
yes you can proceed

Great! Let's dive deeper into PCI and then also touch on PCI Express (PCIe) since it’s the modern standard.
1. How PCI Works (Traditional PCI)
Architecture:

PCI is a parallel bus architecture.

It allows multiple devices to share a common communication path called a bus.

The bus has multiple lines: address lines, data lines, and control lines.

Each device connected to the bus can communicate with the CPU or memory by placing addresses and data on the bus.

Bus Characteristics:

Typical PCI bus width: 32-bit or 64-bit.

Clock speeds: Usually 33 MHz or 66 MHz.

Max data transfer rate (for 32-bit, 33 MHz): 133 MB/s.

Communication:

Devices have unique bus/device/function addresses.

Supports bus mastering, meaning devices can initiate transactions (DMA) without CPU intervention.

Uses interrupts to signal events to CPU (like data ready).

Plug and Play:

Devices have configuration space (256 bytes per device).

The system BIOS or OS scans the PCI bus during boot to discover devices and configure resources (IRQ, memory addresses).

2. Limitations of Traditional PCI

Parallel bus with shared lines causes bandwidth bottlenecks as devices increase.

Limited scalability and slower speeds.

Signal integrity issues at higher frequencies.

Fixed maximum bandwidth per bus.

3. PCI Express (PCIe) – The Modern Standard
Overview:

PCIe is a serial point-to-point link architecture.

Replaced PCI and PCI-X for most purposes.

Much faster and scalable.

Key Features:

Uses lanes, each lane has two differential signaling pairs (one for transmit, one for receive).

Typical PCIe link widths: x1, x4, x8, x16 lanes.

Data rate per lane depends on PCIe generation:

Gen1: 2.5 GT/s (gigatransfers per second) ~250 MB/s per lane

Gen2: 5 GT/s (~500 MB/s per lane)

Gen3: 8 GT/s (~1 GB/s per lane)

Gen4: 16 GT/s (~2 GB/s per lane)

Gen5 and newer continue increasing

Architecture:

Each device connects directly to the host through dedicated links.

Full-duplex communication (can send and receive simultaneously).

Supports hot plugging and dynamic resource allocation.

Uses packets to transmit data, similar to networking.

Advantages:

Much higher bandwidth than PCI.

Scalable by increasing the number of lanes.

Better signal integrity and lower latency.

Supports advanced error detection and correction.

Summary Comparison:
Feature PCI (Traditional) PCI Express (PCIe)
Communication Parallel bus Serial point-to-point
Speed Up to 133 MB/s (32-bit, 33 MHz) Up to multiple GB/s depending on lanes & gen
Scalability Limited by bus sharing Scalable by number of lanes
Bus Sharing Shared bus for all devices Dedicated links per device
Plug and Play Yes Yes
Duplex Half-duplex Full-duplex
## PCI (Peripheral Component Interconnect)
- Type: Parallel bus interface for connecting internal expansion cards to motherboard.
- Purpose: Connect internal devices like network cards, sound cards, graphics cards (older ones).
- Speed: Up to 133 MB/s (32-bit, 33 MHz).
- Bus: Shared parallel bus among multiple devices.
- Topology: Multiple devices share the same bus, with fixed addressing.
- Use case: Mostly legacy; replaced by PCIe in modern systems.
- Connection: Internal motherboard slot.

## 2. PCI Express (PCIe)
- Type: High-speed serial point-to-point interface.
- Purpose: Connect internal devices (graphics cards, SSDs, network cards) with very high bandwidth.
- Speed: Scales with generations and lanes:
  - PCIe Gen3 x16 = ~16 GB/s
  - PCIe Gen4 x16 = ~32 GB/s
- Bus: Dedicated serial lanes per device.
- Topology: Point-to-point, each device has a dedicated link to the host.
- Use case: Modern internal expansion for graphics cards, NVMe SSDs, high-speed network cards.
- Connection: Internal motherboard slot (often large x16 slot for GPUs).

## 3. USB 3.0 (Universal Serial Bus 3.0)
- Type: External serial interface for connecting peripherals.
- Purpose: Connect external devices like flash drives, external hard disks, keyboards, mice, webcams, etc.
- Speed: Up to 5 Gbps (approx 625 MB/s).
- Bus: Shared serial bus with host controller and multiple devices connected via hubs.
- Topology: Tree topology with hubs and devices.
- Use case: External connectivity standard for data transfer and device charging.
- Connection: External USB ports with USB Type-A or other connectors.

The bandwidth of a bus means the maximum amount of data it can transfer per second.
It depends on two main factors:
1. Bus width (number of data lines — bits transferred in parallel per clock cycle)
2. Clock frequency (number of cycles per second)
The formula is:
 (bytes/sec) width (bits) frequency (Hz)Bandwidth (bytes/sec)=8Bus width (bits)​×Clock frequency (Hz)
SB is a standardized interface that allows for the connection and communication between computers and various electronic devices.
It facilitates both data transfer and power delivery.
USB is considered "universal" because it's widely compatible across different devices and operating systems.
It's also "serial" because data is transmitted one bit at a time, which is an efficient method of communication.
Key Features:
Plug and Play:
USB allows devices to be connected and automatically recognized by the computer, without needing to install drivers or restart the system.
Hot Swappable:
You can connect and disconnect USB devices while the computer is running, a feature known as "hot swapping".
Power Delivery:
USB provides a small amount of power to connected devices, allowing them to be charged or function without needing a separate power supply.
Various Connectors:
There are different types of USB connectors, including Type-A, Type-B, Type-C, and Micro-B, each designed for specific devices and functionalities.

In USB (and PCI/PCIe too), Device ID and Vendor ID are unique numeric identifiers used to tell the operating system exactly what hardware is connected, so the right driver can be loaded automatically.

## 1. Vendor ID (VID)
- A 16-bit number assigned by the USB Implementers Forum (USB-IF) to each manufacturer.
- It’s like a company’s unique registration number in the USB world.
- Example:
  - Intel → 0x8086
  - Microsoft → 0x045E
  - Logitech → 0x046D

## 2. Product ID / Device ID (PID)
- A 16-bit number assigned by the manufacturer.
- Identifies the specific product/model under that vendor.
- Example (Logitech VID = 0x046D):
  - Logitech MX Master Mouse → 0xC52B
  - Logitech Webcam C920 → 0x082D

## 3. Why it’s needed
- When you plug in a USB device, the host sends a GET_DESCRIPTOR request.
- The device responds with:
  - VID (Vendor ID)
  - PID (Product ID)
  - Device class, subclass, protocol, etc.
- The OS looks in its driver database:
  - If a driver for (VID, PID) is found → load it.
  - If not → prompt for driver installation.

## 4. Example
If you plug in a USB flash drive:
- VID: 0x0781 → SanDisk
- PID: 0x5567 → Cruzer Blade 32GB
- OS finds "SanDisk Cruzer Blade driver" and loads it.

## 1. Motherboard PCIe Slots & Lanes
- What you see: The long black/blue slots on the motherboard labeled x1, x4, x8, x16.
- What they do: They are roads for data between the CPU and your device.
- Lanes = number of separate roads.
  - x1 → 1 road each way (Tx, Rx) → slower.
  - x16 → 16 roads each way → much faster.
- Example:
  - A graphics card usually needs x16 (16 lanes) for high bandwidth.
  - A sound card might only need x1.

## 2. Endpoint Devices
- These are the things you plug into those slots.
  - Examples: Graphics card, NVMe SSD, network card, FPGA board.
- Inside each device:
  - A PCIe controller that talks to the motherboard.
  - Registers for configuration (like switches and knobs for the driver to use).
  - Optional RAM or buffers for storing/transferring data.
  - Ability to interrupt the CPU when something happens.

## 3. Root Complex
- The brain on the CPU/motherboard that manages all PCIe traffic.
- The Root Complex:
  - Detects devices when the system starts.
  - Decides how much "road space" (bandwidth) each device gets.
  - Assigns memory addresses (so the CPU knows where to talk to the device).
  - Connects PCIe devices to system RAM.

## 4. Link Training & Enumeration
When you power on:
1. Link Training (handshake between CPU and device):
  1. "Hey device, can you go at Gen4 speed?"
  2. "Yes, but I only have 8 lanes."
  3. "Alright, let’s use Gen4 x8."
2. Enumeration:
  1. CPU reads the device’s Vendor ID (who made it) and Device ID (what it is).
  2. Assigns it:
    1. Bus number
    2. Device number
    3. Function number (some devices have multiple functions, like a GPU with an audio function)
  3. Reserves memory areas (BARs) for the device.

## 5. BARs (Base Address Registers)
- Each PCIe device asks for a chunk of memory space for its registers or data.
- Example:
  - BAR0 = 4 KB → control registers (switches/buttons the driver can set/read)
  - BAR1 = 8 MB → device’s local memory or buffers
- The CPU will use these addresses to talk to the device using MMIO (Memory Mapped I/O).

## 6. Interrupt Mechanisms
When the device needs the CPU’s attention, it sends an interrupt:
1. Legacy Interrupts (INTx):
  1. Old style, multiple devices may share the same interrupt → CPU must check who called.
2. MSI (Message Signaled Interrupts):
  1. Device sends a small message to a special CPU memory location → no sharing, faster.
3. MSI-X:
  1. Like MSI, but can have many interrupt lines → different parts of the device can signal separately (e.g., multi-queue network cards).

💡 Putting it all together:
1. You plug a PCIe card into the motherboard slot.
2. The Root Complex detects it, negotiates speed & lanes.
3. The CPU assigns BARs and interrupt numbers.
4. Your driver uses those BARs to control the device.
5. Data flows through PCIe lanes using MMIO or DMA.
6. The device uses interrupts to notify the CPU when it’s done.

PCIe at its core

PCIe (Peripheral Component Interconnect Express) is a high-speed serial, point-to-point interconnect between the CPU/chipset (Root Complex) and devices (Endpoints).

It replaced parallel PCI for better speed and scalability.

Each connection is a Link, made up of lanes.

Each lane can be:

Gen1 → 2.5 GT/s (~250 MB/s per direction)

Gen2 → 5 GT/s (~500 MB/s per direction)

Gen3 → 8 GT/s (~985 MB/s per direction)

Gen4 → 16 GT/s (~1969 MB/s per direction)

Gen5 → 32 GT/s (~3938 MB/s per direction)

Gen6 → 64 GT/s (~7876 MB/s per direction)

Lanes can be combined (x1, x4, x8, x16) to increase throughput.
2️⃣ PCIe Topology

PCIe forms a tree-like hierarchy:

[ CPU / Root Complex ] (Bus 0)
| Root Ports
+----[ Endpoint: GPU ]
+----[ PCIe Switch ]
+----[ Endpoint: NVMe SSD ]
+----[ Endpoint: NIC ]

Root Complex (RC) → connects CPU/memory to PCIe devices.

Root Port → the “exit” from RC to a PCIe link.

Switch → expands one Root Port into multiple downstream ports.

Endpoint (EP) → an actual PCIe device that performs a function (GPU, NIC, SSD).

Bridge → logical entity connecting two buses (Switch ports are bridges).

3️⃣ PCIe Addressing Model

PCIe still uses the PCI logical addressing scheme:

Bus : Device : Function

Bus → logical grouping number (0–255 possible)

Device → position on that bus (0–31 possible)

Function → sub-function inside a device (0–7 possible)

So, maximum addressing space =
256 buses × 32 devices/bus × 8 functions/device = 65,536 functions total.

💡 In practice:

You won’t reach the theoretical max because hardware (chipset, switches) limits fan-out.

Consumer motherboards usually have 4–8 Root Ports; big servers with PCIe switches can get hundreds of devices.

4️⃣ PCIe Configuration Space

This is per-device metadata + control registers.
Purpose:

Identifies the device (Vendor ID, Device ID)

States capabilities (supported speeds, lanes, MSI/MSI-X, etc.)

Holds BARs (Base Address Registers) → tells CPU where the device’s MMIO space lives

Contains status, command bits, and power management controls.

Structure:

First 256 bytes: Standard PCI header (PCI-compatible)

Next space (up to 4KB): Extended PCIe-specific capabilities

Example layout (256-byte standard part):
Offset Field Size
0x00 Vendor ID 2 bytes
0x02 Device ID 2 bytes
0x04 Command Register 2 bytes
0x06 Status Register 2 bytes
0x10 BAR0 4 bytes
0x14 BAR1 4 bytes
… … …
0x3C Interrupt Line / Pin 4 bytes
5️⃣ How Many Devices Can I Connect?

The absolute theoretical limit is from the addressing scheme:

256 buses × 32 devices per bus × 8 functions = 65,536 functions

But in real life:

Root Complex has a limited number of Root Ports (e.g., 4–16 in consumer CPUs, up to ~48 in big Xeons).

PCIe switches can expand that, but they have finite downstream ports.

Electrical & performance constraints (bandwidth sharing) limit practicality.

Example:
If each Root Port → PCIe Switch with 8 downstream ports → each port has one endpoint
→ You can get 8 × number_of_root_ports endpoints.
6️⃣ How Enumeration Uses Config Space

When the system boots:

Root Complex starts at Bus 0.

Reads config space of each possible device (Device 0–31, Function 0–7).

If a device exists, reads its Vendor ID / Device ID.

If device is a bridge (e.g., switch port), it assigns a new Bus Number to the downstream side and repeats scanning.

Assigns BAR addresses so CPU can talk to device registers via MMIO.

7️⃣ Summary

PCIe = high-speed serial point-to-point interconnect in a tree topology.

Addressing = Bus:Device:Function (max 65k functions).

Config Space = per-device metadata & control area, readable/writable by CPU.

Actual number of devices depends on physical Root Ports & switches.

Enumeration = RC scanning config space to discover & configure devices.

If you want, I can draw you a diagram showing PCIe’s physical and logical layout with bus numbering and config space locations so this clicks instantly.
That visual will also make the “limit of devices” part very obvious.

Do you want me to make that?
You said:
can uh explain work flow
ChatGPT said:

Got it — let’s walk through the entire PCIe workflow from power-on to data transfer so you can see how all the pieces (Root Complex, bus numbers, config space, BARs, DMA) fit together.
PCIe Workflow
Step 1 — Power On & Link Training

System powers up.

Each PCIe link (Root Complex ↔ device or switch) performs link training:

Negotiates speed (Gen1–Gen5).

Negotiates lane width (x1, x4, x8, x16).

Links stay in an inactive state until configured.

Step 2 — Enumeration (Bus Scanning)

Root Complex (RC) starts at Bus 0.

For each possible Device Number (0–31) and Function Number (0–7):

Reads Configuration Space at address Bus:Device:Function.

If the read returns a valid Vendor ID, a device exists there.

If the device is a Bridge (e.g., PCIe switch port):

RC assigns a new Bus Number to the downstream side.

Repeats scanning for devices on that new bus.

Result:
A tree of buses with devices assigned Bus:Device:Function addresses.
Step 3 — Resource Assignment

For each discovered device:

RC reads BARs (Base Address Registers) from config space.

Each BAR tells how much address space the device needs (MMIO or I/O).

RC assigns physical address ranges in system memory space to those BARs.

Writes those assigned addresses back into the device’s BAR registers.

Now:

CPU knows where in memory the device’s registers live.

The OS can use MMIO reads/writes to control the device.

Step 4 — Driver Binding

OS checks Vendor ID + Device ID in config space.

Matches them to a driver in the OS.

Calls the driver’s probe() function.

Driver:

Enables the device (pci_enable_device()).

Requests access to BAR regions (pci_request_regions()).

Maps BAR addresses to kernel virtual memory (pci_iomap()).

Step 5 — Device Initialization

Driver writes to the device’s control registers (via MMIO):

Sets mode (e.g., network speed, GPU mode).

Configures DMA addresses if needed.

Enables interrupts (MSI/MSI-X or legacy INTx).

Step 6 — Data Transfer

Two main methods:

A) MMIO Access

CPU directly reads/writes device registers or buffers in BAR space:

iowrite32(value, bar0_base + OFFSET);
val = ioread32(bar0_base + OFFSET);

B) DMA Transfer (common for large data)

Driver allocates a DMA buffer in system RAM:

dma_alloc_coherent(&pdev->dev, size, &dma_handle, GFP_KERNEL);

Driver writes the buffer’s physical address into the device’s control registers (via MMIO).

Device initiates DMA over PCIe:

Reads (DMA-IN) or writes (DMA-OUT) directly to/from host memory.

When done, device sends MSI/MSI-X interrupt to the CPU.

Step 7 — Interrupt Handling

OS interrupt handler runs (registered by driver).

Driver checks device status register (via MMIO) to see what happened.

If DMA completed:

Driver wakes waiting processes.

User-space app can now read/write data.

Step 8 — User-Space Interaction

User-space communicates with the driver via:

/dev/ character device → read(), write(), ioctl().

mmap() for direct BAR access.

sysfs/debugfs entries.

Full Flow in Short

[ Power On ]
↓
Link Training
↓
Enumeration (RC scans buses)
↓
Assign Bus Numbers & BAR addresses
↓
Load Driver (based on Vendor ID / Device ID)
↓
Map BARs → Driver MMIO Access
↓
Driver initializes device (mode, DMA buffers, interrupts)
↓
Data Transfer via MMIO or DMA
↓
Interrupt signals completion
↓
User-space sees results

If you want, I can draw you a step-by-step diagram showing how data flows from CPU → Root Complex → PCIe link → Device → back so you can visualize enumeration, BAR mapping, and DMA in one picture.
That will make this workflow click instantly.
You said:
how to know vendor id is valid or not during enumertion
ChatGPT said:

During PCIe enumeration, the Vendor ID validity check is actually very simple — the PCI/PCIe spec reserves one value (0xFFFF) to mean “no device present”.
1️⃣ Where Vendor ID comes from

Every PCI/PCIe device has a Configuration Space.

The very first 4 bytes at offset 0x00 are:

[ 15:0 ] Vendor ID
[ 31:16 ] Device ID

When the Root Complex or OS reads this address, the device responds with its assigned Vendor ID (from PCI-SIG registry).

2️⃣ Valid vs Invalid Vendor IDs

Valid Vendor ID → A real 16-bit value assigned by PCI-SIG (e.g., 0x8086 for Intel, 0x10DE for NVIDIA, 0x1AF4 for VirtIO).

Invalid Vendor ID → 0xFFFF (all bits 1).
This is defined in the PCI spec to mean "no device present at this Bus:Device:Function".

So during enumeration:

RC tries reading from config space at a given B:D:F.

If read returns 0xFFFF, nothing is there → skip to next device/function.

If read returns anything else, it's a real device.

3️⃣ Example in practice

Pseudo-code for enumeration check:

vendor_id = pci_config_read16(bus, device, function, 0x00);
if (vendor_id == 0xFFFF) {
// No device present
} else {
// Device exists, read device_id too
device_id = pci_config_read16(bus, device, function, 0x02);
}

4️⃣ How to check in Linux

From user-space:

lspci -nn

Example output:

00:1f.6 Ethernet controller [0200]: Intel Corporation Ethernet Connection (7) I219-V [8086:15bc]

8086 = Vendor ID (Intel)

15bc = Device ID

To see raw config space:

sudo lspci -s 00:1f.6 -xxx

The first two bytes will be the Vendor ID.

✅ Key takeaway:
During enumeration, "valid" simply means Vendor ID ≠ 0xFFFF.
If it’s 0xFFFF, there’s no device responding at that address.

If you want, I can also explain how the Root Complex actually performs that read over PCIe (TLP transaction) and why 0xFFFF appears when no device responds — that’s the electrical/protocol side. Would you like me to go that deep?
You said:
es
ChatGPT said:

Alright — let’s dig into how the Root Complex actually knows whether a Vendor ID is valid or not, from the PCIe protocol/electrical perspective.
1️⃣ The Setup: Reading Config Space

When the Root Complex (RC) does enumeration, it uses Configuration Read Requests over PCIe.

PCIe communication is packet-based (Transaction Layer Packets, or TLPs).

A Config Read TLP contains:

Bus Number

Device Number

Function Number

Register Offset (e.g., 0x00 for Vendor ID/Device ID)

Type = Configuration Read

2️⃣ RC Sends a Config Read

Example:

RC wants to check Bus 3, Device 0, Function 0, Offset 0x00.

It sends a Type 0 Config Read TLP (for devices on same bus) or Type 1 (for downstream buses via bridges).

The packet travels down the PCIe hierarchy (root port → switch ports → device).

3️⃣ Device Responds (or Not)

Two possibilities:
A) Device exists at that address

The endpoint’s PCIe Configuration Space logic sees that the B:D:F matches its own.

It sends a Completion TLP back to the RC with 4 bytes of data:

Byte 0-1: Vendor ID (e.g., 0x8086 for Intel)
Byte 2-3: Device ID

RC receives data and continues enumeration.

B) No device at that address

No endpoint claims that B:D:F.

The TLP times out in the hierarchy → PCIe fabric generates a Completer Abort response.

In PCIe spec, a Completer Abort for a config read returns all bits set (0xFFFF) for 16-bit reads (or 0xFFFFFFFF for 32-bit reads).

RC interprets this as "No device present".

4️⃣ Why 0xFFFF Means “No Device”

Historically in PCI:

Config space reads to a non-existent device electrically floated the data lines → pull-up resistors made all bits read as 1.

PCIe kept this convention, but here it’s not electrical floating — it’s the protocol-mandated completion code that signals no valid data.

5️⃣ Protocol Flow Example

Bus 0, Dev 2, Func 0:

RC → Config Read TLP (Bus=0, Dev=2, Func=0, Offset=0x00)
↓
If device exists:
Device → Completion TLP (Data=VendorID/DeviceID)
Else:
PCIe fabric → Completion Abort (Data=0xFFFF)

6️⃣ Visual Sequence

[ Root Complex ]
|
| Config Read Request (B:D:F, offset=0x00)
v
[ PCIe Switch / Link ]
|
+---> Device? Yes → sends VendorID (e.g., 0x10DE)
|
+---> No Device → Completion Abort → RC reads 0xFFFF

✅ Key point:
The Root Complex doesn’t guess — it literally tries to read the Vendor ID over PCIe, and if no device responds, the PCIe protocol guarantees it gets back a “no data” pattern (0xFFFF) via a Completion Abort.

Yes — PCIe is packet-based (unlike old parallel PCI which was signal/clock-based with shared lines).
Let me break it down in detail so you can see exactly how it works from physical signaling up to packet flow.

## 1. PCIe as a Packet-Based Protocol
- PCIe works like a network inside your motherboard — but point-to-point instead of broadcast.
- Data is not sent as raw bytes over wires; it’s broken into packets.
- These packets are called TLPs (Transaction Layer Packets) and DLLPs (Data Link Layer Packets).

## 2. PCIe Layered Architecture
Think of PCIe like a networking stack:
Layer	Role
Transaction Layer	Creates TLPs for memory read/write, I/O, and configuration requests.
Data Link Layer	Adds sequence numbers and CRC (LCRC) for error detection, uses ACK/NAK for retries.
Physical Layer	Serializes data into bit streams, sends over lanes using 8b/10b (Gen1/2) or 128b/130b (Gen3+) encoding.

### Step 1 — Transaction Layer Creates a Request
- CPU (Root Complex) makes a Memory Read request for a certain BAR (Base Address Register) address of the device.
- The Transaction Layer builds a TLP with:
  - Request Type: Memory Read
  - Address: Target address in device memory
  - Length: Number of bytes
  - Requester ID: Who sent it

### Step 2 — Data Link Layer Wraps the TLP
- Adds a sequence number so the receiver can detect lost packets.
- Adds an LCRC (Link CRC) for integrity.
- Sends DLLP ACK or NAK depending on whether it got the packet.

### Step 3 — Physical Layer Sends Data
- Data is serialized into 1, 2, 4, 8, 16, or 32 lanes (depending on link width: x1, x4, x8, x16).
- Sent using differential pairs (Tx+, Tx–, Rx+, Rx–).
- PCIe is full-duplex — request packets can go in one direction while data packets come back in the other.

### Step 4 — Device Responds
- Device’s Transaction Layer sees the Memory Read request.
- Fetches data from its internal memory or register.
- Creates a Completion TLP with the requested data.
- Sends it back through the same process (Transaction → Data Link → Physical).

## 4. Packet Types in PCIe
1. TLPs (Transaction Layer Packets)
  1. Memory Read / Memory Write
  2. I/O Read / I/O Write
  3. Configuration Read / Configuration Write
  4. Completion (with/without data)
2. DLLPs (Data Link Layer Packets)
  1. ACK / NAK for reliability
  2. Flow control updates

## 5. Enumeration and Vendor ID Validation
During enumeration:
1. Root Complex sends Configuration Read TLP to Bus 0, Device 0, Function 0.
2. If device responds, it has:
  1. Vendor ID (first 16 bits in config space)
  2. Device ID
3. Vendor IDs are assigned by PCI-SIG — OS checks them against a known list.
4. If Vendor ID is 0xFFFF, it means no device present.

## 6. Limits on Devices (Bus Structure)
- PCIe still keeps Bus:Device:Function addressing:
  - Bus: 0–255 (8-bit) → 256 buses
  - Device: 0–31 (5-bit) → 32 devices per bus
  - Function: 0–7 (3-bit) → 8 functions per device
- Theoretically: 256 × 32 × 8 = 65,536 functions
  But in reality, limited by motherboard lanes & slot count.